## Slide 1
Non-linear iterative optimization method
for locating particles using HPC techniques
G. Ortega1, J. Lobera2, I. García3, M. P. Arroyo2 and E. M. Garzón1
1Dpt. Computer Architecture and Electronics. University of Almería
2Aragón Institute of Engineering Research (I3A). University of Zaragoza
3Dpt. Computer Architecture. University of Málaga
Heteropar 2014

## Slide 2: Outline
Introduction
Non-Linear ODT model for locating particles (NLODT-P)
Methodology to develop models
GPU computing (Forward procedure)
Validation of NLODT-P
Evaluation of NLODT-P
Conclusions

## Slide 3: Optical Diffraction Tomography (ODT)
ODT characteristics:
  ODT has been recently introduced in several fields.
  High accuracy with non-damaging radiation and its imaging capability to recover information from the object.

## Slide 4: Optical Diffraction Tomography (ODT)
2D holograms
Laser
ODT techniques

## Slide 5: Optical Diffraction Tomography (ODT)
2D holograms
Laser
ODT techniques
A priori
information
INPUTS
Set of seeding particle locations
OUTPUT
Diameter of the particles
Refractive index of particles
Fluid refractive index

## Slide 6: Optical Diffraction Tomography (ODT)
NLODT Preliminary model 2D (proposed by J. Lobera and J.M. Coupland) High computational cost.
  The resolution of large and sparse linear systems of equations of complex numbers in double precision was required.
Linear Optical Diffraction Tomography (LODT)
Non Linear Optical Diffraction Tomography (NLODT)
Overcome the problems of multiple scattering in LODT
High fidelity images
Implementation and validation of a 3D NLODT model for the location of particles

## Slide 7: Non-Linear ODT model for locating particles (NLODT-P)
Helmholtz equation :
where
Er (r) illuminating field.
Es (r)  Scattering field.
n (r)  Refractive index of the object to reconstruct.
f (r) Scattering potential.
Reconstruction problem  Optimization problem
Optimization
Method CG
Estimation
of n(r)

## Slide 8: Non-Linear ODT model for locating particles (NLODT-P)
1: Compute PL(1)
2: It = 2
3: while It < iterMax and Value < threshold do
4: Update n(r)
5: for i = 1, 2, ... until i < Nh do
6: Eis(r) = Forward (Eir(r), n(r))
7: Eir,n(r) = Eis(r) + Eir(r)
8: Eic(r) = Filter (Eis(r), ki0,NA)
9: Eim,n(r) = Forward ((Eic(r) − Eim(r))∗, n(r))
10: Eim,n(r) = Eim,n(r) + (Eic(r) − Eim(r))∗
11: g(r)∗ = g(r)∗ + (Eim,n(r), Eir,n(r))
12: end for
13: gMF (r) = Matched Filtering(g(r), sample)
14: [PL(It), Value] = max(abs(gMF (r)))
15: It = It + 1
16: end
Locate next particle
Initial Iteration
Compute the
updated gradient, g(r)
Iterative
Process
Location of the
1st particle
Update the refractive
index field

## Slide 9: Non-Linear ODT model for locating particles (NLODT-P)
1: Compute PL(1)
2: It = 2
3: while It < iterMax and Value < threshold do
4: Update n(r)
5: for i = 1, 2, ... until i < Nh do
6: Eis(r) = Forward (Eir(r), n(r))
7: Eir,n(r) = Eis(r) + Eir(r)
8: Eic(r) = Filter (Eis(r), ki0,NA)
9: Eim,n(r) = Forward ((Eic(r) − Eim(r))∗, n(r))
10: Eim,n(r) = Eim,n(r) + (Eic(r) − Eim(r))∗
11: g(r)∗ = g(r)∗ + (Eim,n(r), Eir,n(r))
12: end for
13: gMF (r) = Matched Filtering(g(r), sample)
14: [PL(It), Value] = max(abs(gMF (r)))
15: It = It + 1
16: end
Initial Iteration
Iterative
Process
Resolution Helmholtz equation
Resolution Helmholtz equation
95% Runtime

## Slide 10: Methodology to develop models (MATLAB + GPU computing)
Multithreaded
High programming language level
Visualization tools
Libraries: GPUmat, Jacket, Mexfiles
Accelerate procedures with high computational cost: Forward (Helmholtz equation)

## Slide 11: GPU computing (Forward procedure)
11
Green’s Functions
Spatial Discretization (based on FEM)
Large linear system of equations
M is sparse, symmetric and with a
regular pattern
Linear Eliptic Partial
Differential of
Equations (PDE)
Biconjugate Gradient Method (BCG)

## Slide 12: GPU computing (Forward procedure)
Regular Format
dots
saxpy
SpMV
Biconjugate Gradient Method (BCG)

## Slide 13: GPU computing (Forward procedure)
Regularities of M
Complex symmetric matrix
Max 7 nonzeros/row
Nonzeros are located by 7 diagonals
Same values for lateral diagonals (a, b, c)
Mem. Req. (GB) for storing M:
VolTP CRS ELLR-T Reg Format
1603 0.55 0.44 0.06
6403 35.14 28.33 3.91
16003 549.22 442.57 61.04

## Slide 14: GPU computing (Forward procedure)
CUDA interface.
CUBLAS library for saxpy and dot operations.
Optimization techniques:
  The reading of the sparse matrix and data involved in vector operations are coalesced global memory access, this way the bandwidth of global memory is maximized.
  Shared memory and registers are used to store any intermediate data.

## Slide 15: Validation of NLODT-P
Volume to reconstruct
4 particles of 2µm
= 0.633µm
NA = 0.55
Vol= 1603
Nh = 1
A PRIORI INFORMATION:
Diameter of the particles
Refractive index of particles
Fluid refractive index

## Slide 16: Validation of NLODT-P
1ª iteration
Evolution of the gradient of the cost function, g(r)
Evolution of the distribution of the refractive index, n(r)
4ª iteration
2ª iteration
3ª iteration

## Slide 17: Evaluation of NLODT-P
 | Tesla M2090
Peak performance (double precision) (GFlops) | 665
Peak performance (simple precision) (GFlops) | 1331
Device memory (GB) | 6
Clock rate (GHz) | 1.3
Memory bandwidth (GBytes/sec ) | 177
Multiprocessors | 16
CUDA cores | 512
Compute Capability | 2
Year architecture | 2011
DRAM TYPE | GDDR5
GPU architecture (CUDA programming interface)
Multicore: Intel Xeon E5620 (8 cores)
(2.4 GHz, 48 GB RAM) under Linux.

## Slide 18: Evaluation of NLODT-P
4 particles of 0.5µm
= 0.633µm
NA = 0.55
Vol= 2003-2803
Nh = 3
iterMax=4

## Slide 19: Conclusions
A physical model of Non-linear ODT for the application in velocimetry techniques has been implemented and evaluated over 3D prototypes of interest (NLODT-P).
    MATLAB framework  productivity in the generation of codes.
    Integration of GPU computing and MATLAB  Mex-files.
    Illustration of a methodology for the development of scientific applications.
    GPU memory is a limiting factor.
  Future works: distributed implementation.

## Slide 20: Conclusions
Distributed version of Forward
Hybrid Implementation (BCG-3DH)
MultiGPU Implementation
Multicore CPU Implementation
+
Solve larger problems
Runtime is reduced
CUDA
Message Passing Interface (MPI)

## Slide 21: Conclusions
Runtime (s) of 1000 iterations of the BCG-3DH using
8GPUs+8CPUs versus 8GPUs
Vol

## Slide 22: Contraportada